Successful Business Case: Telecommunication Product allowing eHealth Companies to Extend Lifetime of Their PSTN Devices

B. Marc

eDevice, Merignac, France

Large Telehealth companies provide solutions for monitoring patients that have been released from hospital and that require either short term (30-90 days) or long term (for life) monitoring. Traditionally these monitoring devices allow sending medical data for analysis to physicians and nurses over standard fixed telephone lines (PSTN). The evolving nature of telecommunication infrastructure has resulted in the removal of PSTN lines in many places, a trend which is growing fast and will eventually result in few or no traditional phone lines being available due to commercial and regulatory sunset trends. In addition, due to advances in medicine and treatment, patients are far more mobile nowadays than in the past. The overall outcome of these trends is that it has become difficult to rely on the availability of a PSTN line for patient monitoring. The BridgeD130 / WireX and Global Cellular Service enable patient monitoring devices that connect over regular fixed telephone lines (PSTN / POTS) to be switched to cellular communication without requiring any changes to the monitoring device. It allows healthcare companies to extend lifetime of their Remote Monitoring Solutions. eDevice's offer consists of in-house developed hardware that replaces the phone line and enables cellular communication (BridgeD130 / WireX) and a global cellular communication service that allows the BridgeD130 / WireX to send and receive data from anywhere around the world where a GPRS (GSM) data network available. This provides both a global solution to companies with patients around the world and a solution to patients that travel internationally. The global cellular service has been designed from the bottom up for Healthcare companies only and consists of two redundant Network Operation Centres in Europe and the USA that are manned 24/7. A web-based interface allows Healthcare companies to manage their units worldwide from one central location, troubleshoot, and control usage. The solution has been adopted by companies such as Medtronic, Philips, and Honeywell. It’s used in dozens of countries around the world by tens of thousands of users and the list of countries is expanding every month.

Keywords: telecommunication, wireless, market trends, mobile